## Slide 1: Resampling Analysis

## Slide 2: Theorical Analysis
Matlab usage of real ‘resample’ function
  Example :
    Input signal frequency : 10 Khz
    Input signal frequency sampling : 48 Khz
    Output signal frequency sampling : 48,510 Khz

## Slide 3: Theorical Analysis
Script version of Atmel AVR32 DSP resample function without the FIR Calculation stage (Matlab compute FIR coefficients)
  Example :
    Input signal frequency : 10 Khz
    Input signal frequency sampling : 48 Khz
    Output signal frequency sampling : 48,510 Khz
The gain is below 1 due to reduction of filter bandwith gain.

## Slide 4: Theorical Analysis
Script version of Atmel AVR32 DSP resample function without the FIR Calculation stage (Matlab compute FIR coefficients)
  Example :
    Input signal frequency : [0;22 Khz]
    Input signal frequency sampling : 44 Khz
    Output signal frequency sampling : 48,510 Khz
-3dB gain obtained at 17KHz
The gain is around -6dB due to reduction of filter bandwith gain.

## Slide 5: Analysis
Next Step
  1) Use Atmel AVR32 DSP resample function with precalculated Matlab filter coefficients and compare the two results
  2) Compute the filter response of Atmel AVR32 DSP resample function in the frequency range [0;20Khz].

## Slide 6: Practical Analysis
Step1) Embedded release of Atmel AVR32 DSP resample function without the FIR Calculation stage (Matlab compute FIR coefficients)
  Example :
    Input signal frequency : 10 Khz
    Input signal frequency sampling : 44,1 Khz
    Output signal frequency sampling : 48 Khz
Only a temporal shift is observed, same frequency fresponse.

## Slide 7: Practical Analysis
Step1 bis) Embedded release of Atmel AVR32 DSP resample function with Atmel AVR32 DSP FIR Calculation stage
  Example :
    Input signal frequency : 10 Khz
    Input signal frequency sampling : 44,1 Khz
    Output signal frequency sampling : 48 Khz
Only a temporal shift is observed, same frequency fresponse.
Script result
Embedded result

## Slide 8: Practical Analysis
Step 2) Compute the filter response of Atmel AVR32 DSP resample function in the frequency range [0;20Khz].
  Example :
    Input signal frequency : [0;20Khz].
    Input signal frequency sampling : 44 Khz
    Output signal frequency sampling : 48.510 Khz
Gain in the band = -21dB
Fc (-3dB) = 17.8 Khz
Filter order = 6

## Slide 9: Practical Analysis
Step 2 bis) Compute the filter response of Atmel AVR32 DSP resample function in the frequency range [0;20Khz].
  Example :
    Input signal frequency : [0;20Khz].
    Input signal frequency sampling : 32 Khz
    Output signal frequency sampling : 44.1 Khz

## Slide 10: Practical Analysis
Step 2 bis 1) Compute the filter response of Atmel AVR32 DSP resample function in the frequency range [0;20Khz].
  Example :
    Input signal frequency : [0;20Khz].
    Input signal frequency sampling : 48 Khz
    Output signal frequency sampling : 48.51 Khz